## Slide 1: SecureGPS
Florida International University · College of Engineering & Computing · Senior Cybersecurity Capstone · Spring 2026
github.com/dbikowicz/GPSSpoofDetector · Faculty Advisor: Prof. Masoud Sadjadi · Spring 2026
GPS Spoofing Detection System
Team Lead
Daniel Bikowicz
Product Owner
Helen Gomez
Nahahme Bar'Ysrael · Omar Adel Alali · Matthew Clayton
CIS · Senior Capstone · Spring 2026 · 15-minute presentation

## Slide 2
01 PROBLEM DEFINITION
THE THREAT
GPS spoofing broadcasts counterfeit GPS signals to deceive receivers into reporting a false location — a largely untapped market for defensive tooling.
Fleet & Logistics
Mask vehicle theft, unauthorized detours
Ride-Share
Fake surge zones, manipulate fares
Critical Infrastructure
Military, aviation, maritime GPS
Autonomous Vehicles
Misdirect GPS-dependent cars
Geofence Bypass
Drones, parolees, restricted zones
WHY IT MATTERS
$300
Off-the-shelf SDR attack kit
NONE
Authentication in civilian GPS signals
2017
Black Sea maritime spoofing attack
OUR SOLUTION — SecureGPS
Server-side GPS spoofing detection that analyzes incoming telemetry in real-time — no hardware modification required.
Works with any GPS device reporting over HTTP
Lightweight, software-only — no hardware changes
SOC-style dashboard with forensic audit trail

## Slide 3
02 SYSTEM ARCHITECTURE
GPS DEVICES / FLEET driver_01 · driver_02 · … · driver_08 | 
 | HTTP POST /ingest
DETECTION ENGINE (FastAPI / Python)
Speed > 60 m/s
Geofence Zone
HDOP < 0.5
Bearing 160°+
Severity Scoring
HMAC-SHA256
SQLite Storage
DATABASE (SQLite) events: id · device_id · timestamp · lat · lon · decision · severity · signature | 
 | REST API (JSON)
SOC DASHBOARD (HTML / Leaflet.js)
Real-time map · Alert feed · Device profiles · Forensic verification · ACK workflow
TECHNOLOGY STACK
Layer Technology Purpose |  | 
Backend | FastAPI / Python 3.10+ | Async REST API & detection engine
Database | SQLite3 | Persistent event storage
Validation | Pydantic | Input schema enforcement
Frontend | HTML5 / Vanilla JS | Dashboard interface
Mapping | Leaflet.js + MarkerCluster | Geospatial visualization
Map Tiles | CartoDB Dark | Dark tactical map layer
Crypto | HMAC-SHA256 | Event integrity signing
Templating | Jinja2 | Server-side rendering

## Slide 4: Unrealistic Speed
03 DETECTION METHODS
CRITICAL / HIGH
Teleportation Detection
Haversine formula: great-circle distance between consecutive GPS points
Derives speed from distance ÷ time delta
Threshold: > 60 m/s (~135 mph) → CHALLENGE
Catches teleportation (Miami → NYC in 4 seconds)
MEDIUM
Geofence Violation
Boundary Monitoring
Authorized zone: South Florida lat 25–27°, lon -81° to -79.5°
Any reading outside all defined geofences is challenged
Covers FIU / Miami-Dade operational area
Extensible: multiple zones supported
HDOP Anomaly
Signal Quality Spoofing
LOW
— HDOP (Horizontal Dilution of Precision) measures signal quality
— Real-world values typically 0.8–2.0+
— Threshold: HDOP < 0.5 → unnaturally perfect signal
Rapid Bearing Change
Direction Reversal
MEDIUM
— Computes forward azimuth between consecutive GPS points
— Threshold: bearing change > 160° AND speed > 20 m/s
— A vehicle cannot 180°-reverse at highway speed legitimately
— Spoofers broadcast from one point → artificially low HDOP
CRITICAL — 2+ detections or speed >1000 m/s MEDIUM — Geofence or bearing anomaly
— Speed gate prevents false positives on stationary devices
LOW — HDOP anomaly only ALLOW — All checks passed

## Slide 5
04 SOC DASHBOARD & FEATURES
Geofence overlay — South Florida zone
Forensic HMAC verification
KEY FEATURES
Real-Time Map
Leaflet + cluster, color-coded markers
Alert Feed
Severity tiers, Pending / Acked / All
Device Profiles
Route history, polylines, event log
Toast Notifications
Batched alerts, 1.5 s grouping window
Forensic Verify
HMAC-SHA256 per-event signature check
ACK Workflow
SOC triage with analyst comments
Live Stats
Events / Alerts / Pending / Devices
12 REST API endpoints · 3-second poll · SQLite

## Slide 6: LIVE DEMO
SecureGPS · GPS Threat Detection & Investigation Console · FIU CEC · Spring 2026
GPS Spoofing Attacks — Live in Action
Red markers → attack detected
Toast alerts firing in real-time
Alert feed severity tiers
Forensic HMAC verification

## Slide 7: 05 TESTING & EVALUATION RESULTS
100%
True Positive Rate
All 4 attack types detected
0%
False Positive Rate
Zero clean routes flagged
~85
GPS Readings Tested
Across 8 simulated drivers
<50ms
Detection Latency
Per event, in-memory lookup
DETECTION ACCURACY
Attack Type Scenario Severity Result |  |  | 
Teleportation | Miami → NYC in 4 seconds | CRITICAL | PASS ✓
Geofence Violation | Drift past latitude 27.0° | MEDIUM | PASS ✓
HDOP Spoofing | HDOP = 0.1 (impossibly perfect) | LOW | PASS ✓
Bearing Reversal | 180° U-turn at 30 m/s on I-95 | MEDIUM | PASS ✓
Normal Driving ×5 | Realistic Miami routes | ALLOW | PASS ✓ 0 FP
driver_01 — Teleportation: Miami → NYC (speed ~2,515 m/s)
INTEGRITY VERIFICATION
HMAC-SHA256 verified for all stored events
Tamper detection: field edits cause sig mismatch
Constant-time compare prevents timing attacks
100% severity tier accuracy across all scenarios

## Slide 8
06 CHALLENGES & LESSONS LEARNED
TECHNICAL CHALLENGES
Real-Time Map Integration
Getting Leaflet to update smoothly with incoming events: marker
deduplication, separate clean/alert clusters, and preventing polling from causing visual glitches.
Stateful Detection Across Requests
Speed and bearing require per-device state. Async request handling needed careful design of the last_point dictionary to avoid race conditions.
Haversine & Bearing Math
Implemented from scratch — radian/degree conversion, antimeridian edge cases, validating results against real known distances.
Severity Scoring Design
Combining 4 independent signals into a meaningful tier hierarchy.
Multi-trigger escalation (2+ detections → CRITICAL) required careful logic.
Threshold Tuning
Balancing 60 m/s speed, 160° bearing, and HDOP 0.5 to catch attacks without false positives on legitimate edge cases.
LESSONS LEARNED
Multi-Method Detection Is Essential
No single heuristic catches all spoofing. Speed misses slow drift; geofencing misses in-zone attacks. Layering provides defense-in-depth.
Interleave Clean Data With Attacks
Early demos only showed attacks. Adding 5 clean driver phases dramatically improved demo clarity and audience understanding.
Cryptographic Logging = Accountability
HMAC signing transforms a log into a forensic evidence chain — valuable for incident response and legal proceedings.
SOC Workflow Matters
The acknowledgment system mirrors real SOC triage, making the tool feel production-realistic rather than academic.
Geographic Realism Sells the Demo
Real Miami coordinates (Biscayne Blvd, I-95, Key Biscayne) make the demo tangible and relatable to the audience.

## Slide 9
07 FUTURE WORK
NEAR-TERM IMPROVEMENTS
LONG-TERM VISION
01 | Machine Learning Integration Isolation Forest / LOF to detect subtle slow-drift spoofing that rule-based thresholds miss.
02 | Kalman Filter Smoothing Distinguish genuine GPS noise from spoofing-induced jumps, reducing false positives.
03 | Multi-Satellite Validation Cross-reference GPS with GLONASS, Galileo, or BeiDou to detect single-constellation attacks.
04 | User Authentication & RBAC Login system with analyst / admin / viewer roles for multi-user SOC deployment.
05 | WebSocket Push Notifications Replace polling with real-time push; integrate with Splunk, Elastic, PagerDuty, Slack.
06 | Fleet-Wide Correlation Detect coordinated spoofing attacks targeting multiple vehicles simultaneously.
07 | Cloud Deployment (Docker/AWS) Containerize, auto-scale, enable API key auth for multi-tenant cloud operation.
08 | RAIM Integration Hardware-level integrity via Receiver Autonomous Integrity Monitoring for enterprise use.

## Slide 10: Questions?
Florida International University · Senior Cybersecurity Capstone · Spring 2026
github.com/dbikowicz/GPSSpoofDetector
SecureGPS — GPS Spoofing Detection System
Daniel Bikowicz · Helen Gomez · Nahahme Bar'Ysrael · Omar Adel Alali · Matthew Clayton
Faculty Advisor: Prof. Masoud Sadjadi · CIS 4951 · FIU SCIS