## Slide 1: Water Sampling with Applied Microcontrollers Students: Jesus Elespuru, Angie Martinez, Steven Luque, Christopher Perez Mentor: Dr. Gregory Murad Reis, CREST; School of Computing and Information Science; College of Engineering and Computing Instructor/Faculty: Seyed-Masoud Sadjadi, Florida International University

## Slide 2: Water Sampling with Applied Microcontrollers Meet the Team
Jesus Elespuru - Product Owner
Marine Robotics
Backend Developer
Data Collection
Angie Martinez - Team Lead
Web Developer
Software Design
Project Management
Steven Luque - Team Member
Hardware Design
Wiring Integration
Christopher Perez - Team Member
Mathematics & Circuit Analysis
Temperature Limit Analysis

## Slide 3: Water Sampling with Applied Microcontrollers Introduction
Biscayne Bay faces a number of threats right off Miami’s coastline.
  Environmental factors such as pollution, rising water temperatures, and human activity are damaging our ecosystems.
Manual sampling has been used in recent efforts but this is not efficient.
  Time-consuming, costly, and limited coverage.
  Only provide localized data but miss large-scale, dynamic changes.
Time is essence.
  A scalable, efficient, and autonomous solution can help slow down the damages and detect fish kill before it happens.
Autonomous Surface Vehicles (ASVs) can help us get there.
  Combines automated operations, modular design, and real-time data collection/feedback.
  Enhances efficiency and scalability in water quality and health.
Notes: Notes for Reference:
Threats to Biscayne Bay:
  Pollution sources: Urban runoff, sewage discharge, and marine litter.
  Rising water temperatures: Affect marine life, including coral reefs and fish species.
  Human activity: Coastal development and boating disrupt habitats.
Traditional Monitoring Limitations:
  Manual sampling involves significant labor and costs.
  Limited spatial and temporal resolution makes it unsuitable for dynamic environments.
  Fixed stations provide valuable data but are static and cannot capture broader ecosystem changes.
Autonomous Surface Vehicle (ASV) Features:
  Operates without human intervention, reducing manpower costs.
  Modular design allows easy integration of sensors and system upgrades.
  Real-time data transmission enables immediate access to water quality metrics.
  Scalable system can cover large areas and adapt to different monitoring needs.
Applications of ASV:
  Monitor pollution hotspots.
  Study temperature trends in marine ecosystems.
  Enhance environmental decision-making and resource management.

## Slide 4
With marine robotics, we can monitor the environment without disturbing it.

## Slide 5: Methodology
System Design
A lightweight, durable hull equipped with:
  -> Sensors for temperature, pH, salinity, and dissolved oxygen
It is supported by a rechargeable battery for continuous operation.
  -> Uses a solar-powered energy system
  -> Sustainable for environmental use
It has a GPS and Inertial Measurement Unit (IMU) for precise location and orientation.
  -> Predefined algorithms
  -> Obstacle avoidance
Notes: Notes for Reference:
Hull Design:
  Made from durable, lightweight materials to ensure ease of mobility and resilience in marine environments.
  Optimized for stability and minimal drag in water.
Sensor Suite:
  Temperature: Monitors thermal conditions affecting aquatic life.
  pH: Measures acidity or alkalinity, critical for assessing water health.
  Salinity: Tracks salt concentration, vital for marine ecosystems.
  Dissolved Oxygen (DO): Essential for evaluating conditions for aquatic organisms.
Energy System:
  Solar panels reduce environmental impact and operating costs.
  Rechargeable battery ensures continuous operation during low sunlight conditions.
Navigation System:
  GPS: Provides accurate geolocation for route planning and data tagging.
  IMU: Tracks orientation and movement for stable operation.
  Pathfinding: Uses algorithms to adhere to predefined routes, enabling systematic data collection.
  Obstacle Avoidance: Incorporates sensors or algorithms to detect and bypass obstacles, preventing damage and ensuring smooth operations.
Operational Advantages:
  Reduced need for manual intervention.
  Capable of long-term deployment in various aquatic environments.
  Reliable and scalable for diverse monitoring needs.

## Slide 6: Methodology
Data Collection
A microcontroller processes the data collected by sensors for transmission.
Cellular or antenna communication sends this data to a cloud platform.
The platform stores, analyzes, and visualizes the data for users to see.
This platform:
  -> Includes a web and mobile application that enable real-time data monitoring.
  -> Provides status updates and navigation control options.
Notes: Notes for Reference:
Data Processing:
  Microcontroller gathers readings from all sensors.
  Converts raw data into a structured format for transmission.
Data Transmission:
  Cellular communication for areas with network coverage.
  Satellite module ensures connectivity in remote locations.
  Data packets include timestamp, location, and sensor readings for precise analysis.
Cloud Platform:
  Storage: Large-scale, secure data repository for long-term access.
  Analysis: Leverages algorithms to detect trends, anomalies, and patterns.
  Visualization: Interactive dashboards for intuitive understanding of water quality metrics.
User Interfaces:
  Web Application: Accessible on desktops, optimized for in-depth data analysis.
  Mobile Application: Real-time updates on ASV status and water quality for on-the-go monitoring.
  Control Features: Manual navigation adjustments and route planning in case of emergencies or dynamic conditions.
Operational Benefits:
  Immediate access to real-time insights enhances decision-making.
  Scalable for use in multiple locations with centralized data access.
  Intuitive interfaces ensure user-friendly experiences for both professionals and stakeholders.

## Slide 7: Methodology
Testing & Validation
Initial testing before deployment ensured:
-> Sensor accuracy
-> Navigation reliability
-> System integration
Comprehensive testing during and after deployment:
  -> Conducted in Biscayne Bay and Haulover Beach to mimic operational environments.
  -> Tested exposure to factors such as water currents, salinity, etc.
Notes: Notes for Reference:
Initial Testing:
  Sensor Accuracy: Cross-check sensor outputs against standard measurements to confirm reliability.
  Navigation Reliability: Test GPS, IMU, and pathfinding systems for precision and smooth operation.
  System Integration: Ensure all components (sensors, microcontroller, communication modules) work together seamlessly.
Comprehensive Testing:
  Conducted in Biscayne Bay to mimic operational environments.
  Test exposure to factors like water currents, salinity, temperature fluctuations, and debris.
  Validate real-time data transmission via cellular and satellite modules.
Key Performance Metrics:
  Environmental Durability: Ability to withstand rough waters, extreme weather, and prolonged exposure.
  Sensor Accuracy: Consistent and precise readings compared to manual sampling.
  Autonomous Operation: Smooth obstacle avoidance, efficient navigation, and battery sustainability.
Testing Outcomes:
  Identify areas for optimization, such as sensor calibration or energy efficiency.
  Build confidence in system reliability before scaling up or commercial deployment.
  Demonstrate operational viability to stakeholders and funding bodies.
Initial tests ensure sensor accuracy, navigation reliability, and system integration.
Comprehensive testing in Biscayne Bay evaluates the ASV’s performance in real-world conditions, including its ability to withstand environmental challenges, maintain accuracy, and operate autonomously.

## Slide 8: Water Sampling with Applied Microcontrollers Results
Sensors provided reliable readings, verified by calibration and manual sampling comparison.
GPS and IMU systems ensured precise route tracking and effective obstacle avoidance. Solar panels powered daytime operations; rechargeable battery ensured night functionality.
Real-time data transmission to the cloud-platform, which is accessible via the web and mobile apps which led to robust performance across large areas, collecting data autonomously.
Analysis
  Seasonal variations in October recorded higher water temperature than in March (27.58°C vs. 25.03°C)
  Dissolved oxygen increased in variability in October (113.27% with SD: 19.93%) vs. March.
  October’s mean turbidity (147.07 FNU) elevated due to runoff and human activity.
  October saw spikes, indicating higher algal activity.
  March saw stable conditions with lower turbidity and consistent dissolved oxygen levels.
Notes: Notes for Reference:
Sensor Accuracy:
  Regular calibration ensured precision.
  Manual sampling used as a benchmark for data validation.
Navigation Performance:
  Accurate GPS-enabled route adherence.
  IMU facilitated stable orientation and obstacle detection.
  Performance validated across varied aquatic conditions.
Energy Efficiency:
  Solar panels optimized for maximum daylight energy capture.
  Battery capacity tested for prolonged use in low-light scenarios.
Data Transmission:
  Reliable connectivity through cellular/satellite communication.
  Cloud platform ensured secure storage and interactive visualization.
Field Trials:
  Biscayne Bay trials assessed autonomous capabilities in real-world conditions.
  Demonstrated adaptability to environmental challenges like currents and debris.
Water Quality Insights (March–October 2024):
  Temperature Variations: Seasonal increase highlighting warmer October conditions.
  Dissolved Oxygen Variability: Impacted by temperature and biological activity.
  Turbidity Trends: Elevated in October, influenced by stormwater runoff and human impact.
  Algal Activity: Chlorophyll spikes in October suggest eutrophication events.
  Data emphasizes the importance of ASV's role in capturing dynamic environmental changes for conservation planning.
Sensor Accuracy: The ASV’s water quality sensors consistently provided accurate readings for all measured parameters, verified through calibration and comparison with manual sampling techniques.
Navigation Performance: The GPS and IMU systems enabled precise route tracking and reliable obstacle avoidance, ensuring smooth autonomous operation across varied environments.
Energy Efficiency: Solar panels provided continuous power during daylight hours, while the rechargeable battery ensured uninterrupted operation during low-light conditions, such as at night.
Data Transmission: The communication module successfully transmitted data in real-time to the cloud, where it was stored and visualized. Users were able to access this data seamlessly through the provided applications.
Field Trials: In Biscayne Bay, the ASV demonstrated robust performance, autonomously navigating large areas and collecting comprehensive, real-time water quality data.

## Slide 9: Water Sampling with Applied Microcontrollers Conclusion
The ASV offers an efficient, cost-effective alternative to traditional methods.
The user-friendly web and mobile applications provide real-time data for quicker decision-making.
Modular, autonomous design ensures environmental friendliness and extended use.
The several field tests proved the ASV’s reliability and scalability and contributes to improved aquatic ecosystem management.
Seasonal Findings in Biscayne Bay:
October Highlights
  Higher biological activity, turbidity, and temperatures compared to March.
  Chlorophyll spikes indicate increased algal growth, potentially leading to eutrophication.
  Dissolved oxygen variability reflects dynamic ecosystem responses.
March Stability
  Lower turbidity, consistent dissolved oxygen levels, and stable environmental conditions.
Driving Factors:
Warm temperatures, runoff, and human activities influence nutrient influx and sediment disturbance.
Key Implications:
Bay is highly vulnerable to climatic and anthropogenic pressures.
Highlights the need for scalable, real-time monitoring to enable proactive management.
Notes: Notes for Reference:
Scalable Solution:
  Reduces dependence on costly, labor-intensive manual sampling.
  Can expand monitoring coverage for larger or remote areas efficiently.
Real-Time Insights:
  Provides actionable data to policymakers and environmentalists.
  Facilitates timely interventions to address water quality concerns.
Sustainability:
  Modular design supports easy upgrades and long-term usability.
  Autonomous operation reduces carbon footprint compared to traditional methods.
Proven Performance:
  Demonstrated adaptability in Biscayne Bay’s variable conditions.
  Ready for deployment in other aquatic ecosystems worldwide.
Seasonal Water Quality Findings:
  October Variations: Indicators of stress (higher temperatures, turbidity, algal growth).
  Chlorophyll and Eutrophication Risk: Requires close monitoring to prevent long-term damage.
  Dynamic Dissolved Oxygen Levels: Reflect shifting environmental conditions and biological processes.
Implications for Water Management:
  Proactive approaches needed to counteract climatic and human-induced impacts.
  ASV systems are critical for continuous monitoring and sustainable water resource management.
Scalable Solution: The ASV system offers a scalable, efficient, and cost-effective alternative to traditional water quality monitoring methods, capable of covering larger areas with less effort.
Real-Time Insights: By providing real-time data through a user-friendly interface, the system supports quicker and more informed decision-making for environmental preservation.
Sustainability: The modular design and autonomous operation make the ASV both environmentally friendly and practical for extended use.
Proven Performance: Successful testing and field deployment in Biscayne Bay confirm the ASV’s reliability and potential for large-scale applications, contributing to better management and protection of aquatic ecosystems.

## Slide 10
Quick Demo